## Slide 1
Customer Arrives
Command Center chooses Robot Waiter
Waiter goes to customer and asks for order
Chef gets order and starts cooking food
Command Center chooses Robot Server for order
Robot Server receives food from robot arm
Robot Server delivers food
Customers leaves
Robot Café
Human-Robot and Robot-Robot Interaction
Philip Cooksey & Ben Holden
Introduction
Robot Cafe is a restaurant where the food is cooked by humans and served by robots. We have multiple different types of robots all interacting between the customers and chefs i.e. the customers only ever see the robots.
Robots
Customers
Robot Waiter
  Breadth-first search
  Closest customer first (requested to serve)
  Defaults back to birth place when nothing to do
Robot Server
  Same I and III as Robot Waiter
  FIFO customer service
  If multiple orders then waits to get that much food maxing at 3 burgers.
Robot Arm
  Grabs food from conveyor belt
Distributed path planning
Robot Hierarchy : Determines which robot has to move out of the way (lowest moves)
  Servers (numerically ordered)
  Waiters (numerically ordered)
In our world, customers appear at the door given a random change every world step. They then randomly depth-first search for an open table. They request a burger after being asked a random number of times by the waiter. After receiving their burger from the server, they leave searching breath-first search for a door.
Chef’s Kitchen
The Kitchen receives an order from the robot waiter and starts to cook the food if there is an open counter. The food takes 10 steps to make. The food goes on the conveyor belt to the robot arm. If after 15 steps of cooking and the conveyor belt is full the food is thrown away and cooked again.
Command Center
Jobs split evenly between robots
  Each new customer goes to the next robot and cycles back to the first robot.
Jobs split by room location
  We split the room vertically in half
  One Waiter and Server per side
  The back tables are not used as often due to random chance but still have an effect
Café Flow
Experiment
Compare two management styles used by the Command Center and Free For All
1:20 chance for new customer every step
Two Robot Waiters and two Robot Servers
30,000 time steps for each experiment
Customer total time from arrival to departure recorded along with initial time showing up.
The results demonstrate that with the current world setup for the experiment that splitting the room was better for getting customers out faster.
Chart: Jobs Evenly Split Among Robots
Chart: Jobs Split By Room Location
Chart: Time Histograms
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | Above
Room Split | 23 | 885 | 397 | 100 | 27 | 7 | 1 | 0
Jobs Evenly Split | 13 | 745 | 507 | 106 | 14 | 2 | 2 | 0
Free For All | 53 | 507 | 430 | 218 | 100 | 48 | 20 | 14